## Selected Electrical Incidents and Occurrences

First Quarter – January to March, 2004

Date & 	Program	Location	Accident Description

MIS ID #

Accidents - Fatal:

February 27th	Industrial	Gloucester	Worker made contact with the 600 V power leads to the

1050189						compressor motor.  Worker was servicing a roof-mounted

HVAC unit when the fatal contact happened.

Accidents - Critical:

January 15th	Industrial	Oakville		Technician was doing electrostatic testing, brushed up against

1048367						material being tested.  Received a shock, lost consciousness

for a few seconds, taken to hospital.

January 20th	Industrial	North York	Worker was dumping slag from a tandem trailer, box touched

1048527						27 kV overhead line.  Worker received an electrical shock,

vital signs were absent at time of ambulance arrival.  Worker

revived by ambulance crew.

January 28th	Industrial	Etobicoke	Worker was being lifted by a forklift to change light bulbs.

1048913						Worker received a shock, and fell about 12 feet to floor.

Worker received head injuries and some broken ribs.

March 8th	Industrial	Milton		Worker received an electrical shock and lost consciousness.

1050568						A key chain around his neck touched the inside of an electrical

heater.

March 25th	Construction	Georgina	Worker doing work in a water main, received a 120V shock.

1051270						Lost consciousness for a few seconds.  No information given

as to the source of the electrical energy.

March 29th	Construction	Orangeville	Worker received an electrical shock, fell off a ladder.  Worker

1051317						had no vital signs, was revived while being transported to

hospital.  Worker was doing work on lights, they were

supposed to be de-energized.

Accidents - Non-Critical:

January 10th	Industrial	Courtright	Worker was operating a truck, no static straps on the truck.

1053064						Worker claimed to have received an electrical shock, no other

details given.

January 12th	Construction	Mississauga	Worker was untwisting wire to check for voltage, received a

1048189						shock.  No information given on voltage of wires, or of PPE

that worker could have worn for protection.

January 27th	Industrial	North York	Electrician contacted a live terminal while troubleshooting a

1048854						440 V circuit.  Worker taken to hospital.

January 27th	Construction	Mississauga	Worker received an electrical shock, taken to hospital for

1048937						observation.  No information given as to work being done or

equipment involved in the event.

January 30th	Industrial	Niagara Falls	Worker touched an energized wire, received a burn to one

1048986						finger.  No other details of event given.

February 3rd	Construction	Toronto		Worker was directing a fibre-optic cable through a manhole,

1049158						brushed against a neutral cable.  Worker felt a shock, went for

medical assessment.

February 19th	Industrial	Weston		Worker received an electrical shock from touching a live wire.

1049645						No other details of event given.

February 20th	Industrial	London		Worker was installing a digital box in a wall, pushed some

1049795						wires out of the way.  Worker received an electrical shock,

resulting in a small burn on one finger.

February 23rd	Construction	Mississauga	Worker was installing lighting fixtures, had checked for power

1049843						before proceeding.  At end of job, worker was making the last

connections, felt a shock.  Worker’s probe tester had low

batteries, causing false readings.

February 26th	Construction	Toronto		Powerline contact.  Event description stated that there were no

1050158						serious injuries, but gave no other details of the event.

February 27th	Mining		Milton		Worker received an electrical shock while unplugging an

1050199						electrical jack hammer.  Worker taken to hospital.

March 2nd	Construction	Guelph		Worker on a pole, dropped a ratchet handle.  Handle contacted

1050295						8 kV unit that was energized.  Worker received mild shock.

March 3rd	Construction	Ottawa		Worker was doing drilling to install a sprinkler, drill contacted

1050306						a live wire.  Worker received a shock, was taken to hospital.

March 3rd	Construction	Thunder Bay	Electrician made an electrical contact while changing a

1050436						residential meter.

March 3rd	Construction	Toronto		Worker was installing a pipe hanger, contacted a 110 V wire.

1050616						Worker received an electrical shock.

March 8th	Construction	Toronto		Worker doing work on a 600 V panel, panel exploded.

1050466						Worker received burns, taken to hospital,  No information

given on the work he was doing at the time.

March 13th	Industrial	Windsor		Worker received an electrical shock while moving a gel tank.

1051056						The tank’s grounding wire had become loose.

March 13th	Industrial	Stratford		Two workers received an electrical shock while cleaning up

1051301						water from a flood.  Water was about 2 “ deep on the floor,

electrics were still ON.

March 16th	Industrial	Beamsville	Electrician received a burn to his finger.  No other details of

1050893						event were given.

March 16th	Industrial	Burlington	Worker was installing a new breaker in a 240 V panel, when

1050918						an arc occurred.  Worker received burns to hands and face.

March 18th	Industrial	Nepean		Welder turned off the power outside of a spray booth to do

1051047						work.  Spray booth operator noticed the vent system was not

working, turned power back on.  Worker received an electrical

shock, and burns to his hand.

March 19th	Industrial	Woodbridge	Worker received flash burns to face from a fire in an electrical

1051117						panel.  No information given about type of work being done.

March 26th	Industrial	Cambridge	Worker received a shock from touching a steel pillar.  A

1051279						damaged electrical cable was also in contact with the pillar.

March 29th	Industrial	Cambridge	Worker was checking voltage across the terminals on a paint

1051450						machine when an arc occurred.  Worker received burns to  his

hands.

March 31st	Construction	King City	Worker was stripping secondary cable in a trench, received a

1053080						shock.  Voltage of cable not given.

Reportable Incidents - Powerline Contacts:

January 6th	Industrial	Red Lake	Dump truck was dumping its load, tore down the main power

1047883						line.

January 12th	Construction	London		Line crew had coverups in place on the lines.  While moving

1048116						the dielectric jib, two phases moved and contacted.

January 28th	Construction	Nepean		Machine hit buried cable, no details given as to type of

1048912						machine or voltage of cable.

January 30th	Construction	Unionville	Excavator hit an overhead power line.

1049028

February 9th	Construction	Woodstock	Event classified as an electrical occurrence, no description of

1049278						event given.

February 9th	Construction	Grimsby		Contractor cut a buried cable, locates were off.  No

1049300						information given on cable voltage.

February 11th	Construction	Kingston	Event classified as an electrical occurrence, no description of

1049351						event given.

February 18th	Mining		Kenora District	Diamond drill being moved with mast still raised.  Mast

1049831						contacted overhead power line.

February 19th	Construction	Hamilton	Contractor doing trenching, contacted 120 V buried cable.

1049737

February 25th	Construction	Toronto		Worker cut a conduit containing 600 V conductors.

1050148						Knocked off the lighting in the area.

February 25th	Construction	Oakville		Boom truck contacted a primary voltage overhead line.

1050856

February 27th	Construction	Mississauga	Worker digging holes in concrete, dug into a HV duct bank,

1050178						hit cables.  Worker not aware of cables under the concrete.

March 2nd	Construction	Hamilton	Buried 240 V secondary cable was hit while digging.  Locates

1050276						were off by about 20 feet.

March 2nd	Construction	Ottawa		Hydro cable contacted, no other details of event given.

1050429

March 3rd	Construction	Oakville		Digging for a new electrical service, damaged the buried

1050355						27 kV distribution cable.

March 4th	Construction	Mississauga	While excavating for a underground service, hit a buried

1050352						power cable.

March 11th	Construction	Whitby		Dump truck contacted a 8 kV overhead line.

1050819

March 12th	Construction	Stoney Creek	Workers dug up the street lighting cables, 240 V.

1051101

March 23rd	Construction	Brampton	16 kV primary buried cable was cut.  Details of machine being

1051204						used not given.

# DATA SUMMARY - First Quarter

Fatals:		Criticals:	Non-criticals:		Powerline	Electrical

Contacts:	Equipment:

2004		     1		        6		        25			       19		        0

2003		     0		        5		        14			       22		        0

2002		     0		        5		        18			         8		        0

2001		     1		        7		        21			       11		        1

2000		     1		      12		        10			       16		        3

1999		     1		        7		        16			       13		        1

1998		     1		        9		          7			         9		        0

And Finally….

Nothing this quarter was sufficiently off-the-wall to merit inclusion here.  Stay tuned though.

Information taken from Ministry of Labour MIS database

Report prepared: April 14, 2004

Assembled by:	Michael Reiser

Engineer

PSS – Kitchener District

Phone:	(519) 883-5682

FAX:	(519) 883-5694

E-Mail:	mike.reiser@mol.gov.on.ca