## Selected Electrical Incidents and Occurrences

Fourth Quarter - October to December, 2003

Date & 	Program	Location	Accident Description

MIS ID #

Accidents - Fatal:

There were no fatalities of an electrical nature reported to the Ministry of Labour for the fourth quarter of 2003.

Accidents - Critical:

November 3rd	Construction	Toronto		Workers were drilling for a soil sample when they contacted a

1045739 & 1045742 (same event)			buried 27.6 kV power line.  Both workers received burns from

electrical entry and exit wounds to arms and legs.

November 22nd	Industrial	Toronto		Worker was using a multi-meter to check out a fan circuit.

1046450						Meter blew up, worker received burns to hands and face.

November 26th	Construction	Desbarats	Worker was removing conductors from a hydro pole, as

1046585						conductors were removed, pole snapped at base.  Worker was

tied off to the pole, rode the pole to the ground.  No details

given of specific injuries suffered by worker.

December 4th	Industrial	Cambridge	Worker was changing a loose breaker in a 600 V panel,

1046893						breaker shorted out between two of the bus bars.  Worker

received burns to hands and face.

December 4th	Construction	Burlington	Worker was working on a junction box, received a shock.

1047065						Worker fell from ladder, briefly lost consciousness.  Worker

taken to hospital.

December 9th	Construction	Toronto		During cement pouring operations, the boom of the concrete

1047006						pumping truck contacted 27.6 kV overhead power lines.

Two workers received electrical burns to hands and legs, two

other workers were hit by flying debris when one of the truck

tires exploded.

December 12th	Industrial	Scarborough	Maintenance lead hand was trying to troubleshoot a 600 V

1047383						panel with a multimeter.  Flash occurred, worker received

burns to face and hands.

Accidents - Non-Critical:

October 1st	Industrial	Whitby		Worker received an electrical shock while working, taken to

1044695						hospital.  No other details give.

October 6th	Industrial	Hawkesbury	Worker was loading material into a dough maker when he

1044764						received a shock.  No other details of event given.

October 10th	Industrial	Kitchener	Four-year old child received a shock from a child’s ride.

1045986						Child taken to hospital, Ride equipment checked and found to

be defective.

October 16th	Industrial	Hamilton	Worker was cleaning behind a saw, received a shock.

1045292						No information given on source of the shock.

October 17th	Construction	Mississauga	Worker was installing a baffle in an electrical panel, used

1045339						needle-nosed pliers to pick up an energized cable.  Pliers

pinched the wire, worker received a 347 V shock.

October 19th	Industrial	Longlac		Worker received a flash in his eyes from an electrical arc.

1045270						Worker was doing electrical work at the time.

November 10th	Industrial	Toronto		Worker was trying to determine why lights were flickering,

1045974						went to electrical panel.  Tried to fix the problem, received an

electrical shock.

November 13th	Industrial	Cambridge	Worker was working on a panel in an apartment building, flash

1046119						occurred.  Worker received burns to face and hands.

November 14th	Industrial	Thunder Bay	While replacing a damaged hydro pole, the top of the new pole

1046244						contacted the power lines.  Voltage given as 14.4 kV phase-to-

ground, worker suffered step voltage, taken to hospital.

November 17th	Industrial	Toronto		Electrician received an electrical contact while working on an

1046229						electrical panel.  Worker was taken to hospital.

November 19th	Construction	Mississauga	Worker received a shock from 600 V equipment.  No details

1046325						given of work being done at the time.

November 27th	Construction	Gloucester	Electrical apprentice was installing ground wires.  Thought he

1046653						had turned off the power, touched a bus bar.  Received a shock

and flash injuries to his eyes.

November 28th	Construction	London		Electrical contractor received an electrical contact while doing

1046710						work in a dental office.  No details given of the work being

done at the time.

December 1st	Industrial	Barrie		Worker received minor burns to both hands while plugging in

1046759						an appliance to a regular 120 V outlet.  Worker taken to

hospital for treatment.

December 3rd	Construction	Simcoe		Electrical contractor suffered minor burns to his right arm.

1046868						No details given of work being done or nature of accident.

December 6th	Industrial	Longlac		Electrician used a screwdriver to manually override a starter.

1047865						Starter flashed, worker received minor burns to skin.

December 17th	Industrial	Toronto		Worker was replacing an electrical panel, contacted 120 V.

1047471						Taken to hospital then released.

December 18th	Industrial	Kitchener	Utility worker felt a slight tingle on his arm while splicing a

1047679						cable.  Worker taken to hospital then released.

December 19th	Construction	Etobicoke	Worker touched a wire and received an electrical shock.

1047722						Worker thought wires were not energized.  Taken to hospital

and released.

Reportable Incidents - Powerline Contacts:

October 1st	Construction	Ingersoll		Event listed as electrical occurrence, no other details given.

1044647

October 1st	Construction	Cambridge	Event listed as a power line contact, no other details given.

1044691

October 1st	Construction	Niagara-on-the-	Excavator contacted a buried hydro line.

1044806				Lake

October 2nd	Construction	Dryden		Contact made with power line, no injuries reported.  No details

1044696						given of equipment involved or work being done.

October 6th	Construction	Thunder Bay	Telephone crew contacted a buried primary power cable.

1044735						No other details of event given.

October 8th	Industrial	Rockwood	Contact made with primary cable.  No other details of event

1045061						given.

October 9th	Construction	Kingston	Dump truck pulled down an overhead residential service.

1044907

October 9th	Construction	Kitchener	Scaffolding made contact with 240 V residential service.

1044969

October 9th	Construction	Ear Falls		Crane boom contacted 7200 V power line.

1044984

October 10th	Construction	Town of the 	Crane touched a power line.

1044993				Blue Mountain

October 16th	Construction	Vaughan		Event classified as a power line contact.  No other details

1045154						of event given.

October 16th	Construction	Mississauga	Dump truck box hit a guy wire of a hydro pole.  Pole broke

1045164						and came down.

October 21st	Construction	Etobicoke	Workers were ploughing in a new cable when the plow blade

1045318						severed a 600 V buried cable.

October 22nd	Construction	Ottawa		Crane hit a power line.

1045332

October 26th	Construction	Shebandowan	The load on a transporter vehicle contacted a 4160 V

1045483						overhead line.

October 27th	Construction	Ottawa		Dump truck hit a power line.

1045465

November 6th	Construction	Mississauga	Worker was driving a wooden stake, hit a buried 8 kV

1045882						power line.

November 6th	Construction	Thunder Bay	Contact made with a 14 kV power line.  No other details

1045893						given.

November 10th	Construction	Ottawa		Contact made with a buried power line.  No details

1045988						given of equipment involved.

November 10th	Construction	Hamilton	Workers were doing work on a roof, a piece of metal

1046060						flashing fell off the roof and struck a power line.

November 10th	Construction	St. Catherines	Event listed as a power line contact, no other details given.

1046438

November 13th	Construction	Niagara Falls	Dump truck made contact with an overhead power line.

1046076 & 1046132 (same event)

November 14th	Construction	Nepean		Contractor using a multi-directional boring machine,

1046849						cut through a 120/240 residential service.

November 21st	Construction	Ancaster		Dump truck with raised box contacted power lines.

1046451

November 21st	Industrial	Pembroke	Crane contacted overhead power lines.

1046735

November 22nd	Construction	Ancaster		Worker using a chain saw contacted an overhead 4 kV

1046458						power line.

November 26th	Construction	Vaughan		Piping contractor hit and damaged a buried primary cable.

1046656

November 26th	Industrial	Huntington 	Truck contacted a power line at a farm.  No other details

1047182						given.

November 27th	Construction	Kitchener	Back-hoe contacted a 8 kV power line.

1046621

December 2nd	Construction	Newmarket	Dump truck contacted an overhead power line.

1046778

December 3rd	Construction	Guelph		CAT 320 Excavator contacted an overhead power line.

1046829

December 8th	Construction	Niagara Falls	Contact made with buried power cable.  No other details

1047009						of event given.

December 9th	Construction	St. Catherines	Power line contact, no other details given.

1047040

December 11th	Construction	Hillsburg	Excavator contacted overhead power lines while being moved

1047171						from one position to another.

December 12th	Construction	Oakville		Crane made contact with overhead power lines.

1047448

December 17th	Construction	Stratford		Electrical contact made, no other details given.

1047641

December 20th	Construction	Brampton	Backhoe contacted the neutral of an overhead power line.

1047665

# DATA SUMMARY - Fourth Quarter

Fatals:		Criticals:	Non-criticals:		Powerline	Electrical

Contacts:	Equipment:

2003		     0		      7		         19			       37		        0

2002		     0		      4		         15			       37		        1

2001		     5		      9		         28			       33		        1

2000		     2		      8		         15			       30		        1

1999		     2		      7		         21			       30		        1

1998		     1		      8		         15			       29		        2

And Finally…..

December 17th	Industrial	Rexdale		Worker went to stab a cow with a knife.  Cow kicked back,

1047507						worker stabbed himself in the wrist.  Worker taken to hospital

with possible tendon damage, no details given as to the fate of

the cow.

Information taken from Ministry of Labour MIS database

Report prepared:	January 13, 2004

Assembled by:	Michael Reiser

Engineer

PSS – Kitchener District

Phone:	(519) 883-5682

FAX:	(519) 883-5694

E-Mail:	mike.reiser@mol.gov.on.ca