# Electrical Accidents and Incidents

Annual Summary, 1998 to 2001

Table 1: - Number of Incidents by Quarter per Year:

Category	1st Quarter	2nd Quarter	3rd Quarter	4th Quarter		Total

Fatals:

2001		 1		 1		 2		 4*		   8

2000		 1		 2		 2		 2		   7

1999		 1		 2		 3		 2		   8

1998		 1		 2		 5		 1		   9

Criticals:

2001		 7		13		 5		 9		 34

2000		12		  5		 5		 8		 30

1999		 7		  9		11		 7		 34

1998		 9		  4		13		 8		 34

Non-criticals:

2001		21		12		25		28		 86

2000		10		22		26		15		 73

1999		16		22		24		21		 83

1998		 7		17		13		15		 52

Power line contacts:

2001		11		32		44		33		120

2000		16		34		42		30		122

1999		13		32		40		30		115

1998		 9		30		40		29		108

Electrical Equipment:

2001		 1		 2		 1		 1		    5

2000		 3		 1		 0		 1		    5

1999		 1		 0		 0		 1		    2

1998		 0		 0		 2		 2		    4

Total Accidents:

2001		41		60		77		75		253

2000		42		64		75		56		237

1999		38		65		78		61		242

1998		26		53		73		55		207

* Q4 of 2001 had four accidents causing a total of five fatalities.

Commentary for Table 1

In the above table, if a person (not necessarily a worker) was injured during the accident, it would be counted as a fatal, critical, or non-critical depending on the nature of the injury.  Events are placed in the category of power line contacts or electrical equipment incidents only if a person was not injured.

Table 2 - Detailed Summary of Accidents by Specified Cause:

Category	Meters		Equipment being worked	Close proximity	Faulty

on while still live		to live equipment	equipment

Fatals:

2001		    0			    4				  3			  1

2000		    0			    3				  3			  1

1999		    0			    1				  7			  0

1998		    0			    4				  4			  1

Totals		   0			  12				17			 3

Criticals:

2001		    3			  14				  9			  8

2000		    0			  20				  6			  4

1999		    1			  19				 12			  2

1998		    4			  19				 10			  1

Totals		   8			 72				37			15

Non-criticals:

2001		    4			  43				 12			 27

2000		    1			  35				 17			 20

1999		    1			  40				 15			 27

1998		    2			  27				 11			 12

Totals		   8			145				55			86

Overall:

2001		    7			   61				 24			 36

2000		    1			   58				 26			 25

1999		    2			   60				 34			 29

1998		    6			   50				 25			 14

### Grand Total	 16			229			           109		           104

Commentary for Table 2:

The headings are defined as follows;

- Meters, if the direct cause of the accident involved the malfunction of a meter, the accident would be counted here.  It would be considered as a malfunction of the meter even if the cause was the worker using it on the wrong function or scale.

- Equipment being worked on while still live, if the worker was working directly on the piece of electrical equipment.  If a worker caused the fault with his test leads, the accident would be placed here, and not in the Meters column, as the meter itself did not cause the accident.

- Close proximity to live equipment, if the worker did not intend to do anything with the electrical equipment, but accidentally made contact.  Roofing and siding workers losing control of their metal ladders would be placed here.

- Faulty equipment, if the worker was using the equipment properly, but it had a fault, which caused the accident.  Faulty power drills would go here.

Of the 32 fatalities recorded over the past four years, 17 occurred while workers were doing work in close proximity to exposed electrical equipment.  Of these 17 deaths, 7 occurred as workers lost control of aluminum ladders while moving them or placing them in position.  The ladder contacted one or more phases of an overhead line, and as the electrical current flowed through the ladder to ground, some also went through the worker holding the ladder.  With only about 100 milliamperes required to cause ventricular fibrillation in the human body, not much of the available fault current would have to go through the worker to cause death.

In looking at the critical and non-critical accidents, half involved workers doing work directly on electrical equipment while it was still energized.  While the Construction, Industrial and Mining Programs all allow work to be done on or near to exposed electrical equipment while it is still energized, it is only for limited circumstances in which the work is not practical to be done any other way.  Trouble-shooting using a meter or voltage tester would be an example of this.  In all other circumstances, the power must be turned off before the work is started, and while the work is being done on or near to the electrical equipment.

Table 3 - Detailed Summary of Power Line Contacts:

Overhead Lines					Buried Cables

Crane	Dumptruck	Tree felling 	Other			Digging	Other

2001		  16	      22		       5		   43			    27		   7

2000		  15	      10		       3		   59			    32		   3

1999		  11	      26		       2		   48			    27		   1

1998		  10	      17		       8		   39			    27		   7

Totals:	  52	      75		      18		  189			   113		  18

Commentary:

Unless the event description gave clear information on a specific category, the event would be placed in the Overhead Lines – Other category.  With the brief descriptions that are many times phoned into the Ministry of Labour offices, this category collects many of the events by default.

Produced by:	Mike Reiser, P. Eng.,

Engineer,

PSS-Kitchener District

Phone:	(519) 883-5682

FAX:	(519) 883-5694

E-Mail:	mike.reiser@mol.gov.on.ca

Date of issue:	February 26, 2002