## Reported Electrical Incidents and Occurrences

Second Quarter – April to June, 2002

Date & 	Program	Location		Accident Description

MIS ID #

Accidents - Fatal:

June 27th	Industrial	Brampton	Worker was doing troubleshooting, tried to disconnect a 480 V

1018268						power cord to part of the equipment.  Cord still energized,

worker died from the electrical contact.

Accidents - Critical:

April 6th		Industrial	Cornwall	Worker received burns from an electrical arc, also lost

1011352						consciousness for a short while.  No details given on work

being done at time of event.

May 8th		Construction	Forest Hill	Electrician was knocked unconscious from electrical contact,

1011548						taken to hospital.  Worker doing wiring in electrical box, no

other details of event given.

May 23rd	Construction	Brampton	Linesman was feeding lines from equipment into a 4160 V

1012124						switchboard.  Board was still energized, arc occurred.

Worker received severe burns to face and arms.

May 29th		Industrial	Barrie		Worker received a shock from a nearby lightning strike.

1012794 & 1012802 (same event)			Worker was opening a metal-frame exterior door at time of the

strike.  Worker lost consciousness.

June 1st		Industrial	Toronto		Worker was cleaning a display case, received an electrical

1021006						shock, lost consciousness.  No other details given.

June 24th	Construction	Osgoode		Worker was moving a ladder, touched overhead wires.

1015712						Worker received burns to both feet.

June 24th	Construction	Ottawa		Electrical contractor received a shock while working off a

1015736						ladder.  Worker fell off ladder, lost consciousness.

June 25th	Industrial	Guelph		Worker doing work on a 600 amp switchboard.  He received

1018242						an electrical shock, thrown about 20 ft.  Worker lost

consciousness, was also badly bruised.

June 28th	Industrial	Etobicoke	Worker was doing work on an electrical panel.  Part of the

1018329						equipment contacted the energized bus bar, arc occurred.

Worker received burns to face.

Accidents - Non-Critical:

April 3rd		Construction	Toronto		While on a ladder, worker contacted 340 volts.  No details

1012048						given on work being done at time of event.

April 11th	Industrial	North York	Worker cut into a cable, received burns to his face.

1012055

April 16th	Industrial	Oakville		Worker received an electrical contact while inserting work

1020380						into a chroming tank.  A contractor was setting up a newly

repaired rectifier at the same time.

April 23rd	Industrial	Oakville		Worker suffered an electrical contact, taken to hospital and

1028307						released.  No other details of event given.

May 7th		Industrial	Ottawa		Worker was working on an overhead line from a bucket truck.

1018356						High voltage line arced across a contaminated insulator, flash

caused burns to worker’s right hand and face.

May 9th		Industrial	Toronto		Worker was unplugging a light terminal, light shorted, worker

1013525						received an electrical shock.  Worker fell off ladder, landed on

his back.  Worker was taken to hospital.

May 30th		Construction	Markham	Worker received an electrical shock while on a ladder.

1015935						Worker thrown off ladder, no other details of event given.

May 31st		Industrial	Toronto		Worker received a shock from a stun gun, no other details of

1023431						event given.

June 4th		Industrial	Kingston	Supervisor was trying to replace a 600 V fuse, touched the line

1013133						side of the fuse holder.  Disconnect switch was still ON, line

side of holder still energized.  Supervisor taken to hospital.

June 4th		Industrial	Hamilton	Worker was charging accumulator bottles using a hose from

1029595						the tanker truck.  Hose was arcing to the floor, ground strap

only helped for a short time.  Worker picked up the hose and

received a shock, his foot was tingling and numb.

June 17th	Industrial	Windsor		Event description stated “Worker was electrocuted and

1026218						electrician was let go immediately afterwards.”  No other

details of event given.

June 19th	Construction	Mississauga	Worker received an electrical shock while inside a mechanical

1019178						room.  No other details of event given.

June 20th	Industrial	Oshawa		Worker received an electrical shock, taken to hospital.

1018508						No other details of event given.

June 24th	Construction	Bramalea	Worker contacted an existing 600 V cable.  No details given as

1015742						extent of injuries or work being done at the time.

June 24th	Industrial	Waterloo	Maintenance worker received a shock while standing in a

1018443						puddle of water and touching the handle of a metal door.

Water was coming from equipment in the false ceiling area

above the doorway.

June 25th	Construction	Mississauga	Worker received an electrical shock.  No other details of event

1030329						given.

June 26th	Industrial	Markham	Worker made electrical contact, suffered shock and burns to

1017504						his hands.  No details given of work being done.

Reportable Incidents - Powerline Contacts:

April 3rd		Construction	Elmira		Boom of an 8 ton boom truck contacted a 4160 V overhead

1012031						power line.

May 1st 		Construction	Waterloo	Power shovel contacted a buried secondary power line.  Area

1011925						had been marked from an earlier locate.

May 7th		Construction	Toronto		Hoist block from a crane damaged a power cable.

1011859

May 8th		Construction	East Zorra	While installing a drain line, contractor hit neutral of power

1011569				Township	line, breaking the cable.

May 8th		Construction	Zorra 		Delivery truck left the area with its boom raised.

1012005						Boom contacted overhead power line.

May 16th		Industrial	Sturgeon Falls	Backhoe contacted 7200 V overhead line, broke the neutral

1011890						cable.

May 21st		Construction	Sarnia		Contact made with 27 kV overhead power line, no other

1025480						details given.

May 22nd	Construction	Newmarket	Tower crane involved in event.  Chains from the boom hit a

1012027						hydro wire.

May 27th		Construction	Kingston	Contractor broke two phases of a buried power line.

1012152						No locates had been done.

May 28th		Construction	Monteith	Bulldozer contacted primary line.  No other details given.

1012186

May 29th		Construction	Vaughan		Crane contacted 16 kV overhead line.

1012790

May 29th		Construction	Woodstock	Electrical contact made, no other details given.

1012806

May 29th		Mining		Bomby		Electrician cut into 600 V trailing cable extension cord.

1023366				Township	Cable was still energized, arcing but no injuries.

June 1st		Construction	Central Region	Box of dump truck struck overhead 600 V power line.

1020984				Municipality location not given.

June 4th		Construction	North Bay	Event classified as power line contact, no other details given.

1027818

June 4th		Construction	Mississauga	Worker contacted energized cable, no injuries reported.

1030359 & 1030374 (same event)			No other details of event given.

June 6th		Construction	Bracebridge	Contractor contacted the primary buried cable.  No details

1030350						given of equipment involved in event.

June 7th		Industrial	Hagersville	Bucket truck contacted the neutral of a single phase 16 kV

1018470						overhead line.  Cable broke, knocked off the power.

June 10th	Construction	Murray 		Forestry contractor cutting down a tree, limb fell on power

1015708						line.

June 10th	Construction	Oakville		Line crew working on a pole, drilling the pole to install a

1023334						guy anchor.  Contacted primary phase.

June 11th	Construction	Timmins		Excavator struck overhead 2400 V power line.

1013538

June 17th	Construction	Belleville	Forester trimming trees, lower boom of bucket truck contacted

1015517						hydro line.  Line broke.

June 18th	Construction	Welland		Excavator contacted 4160 V buried conductor.

1025837

June 19th	Construction	Wellesley	Dump truck went forwards while box was raised, box caught

1018489						the power line to the residence.

June 20th	Construction	Thamesford	Excavator contacted a buried 2400 V cable.

1015672 & 1020862 (same event)

June 21st		Construction	Eastern Region	Dump truck contacted the neutral of an overhead power line.

1015691				Municipality location not given.

June 24th	Construction	Oakville		Crane cable contacted a 16 kV overhead line.

1023657 & 1023727 (same event)

June 30th	Industrial	Pickle Lake	While creating a fire break, a bulldozer pushed 5 trees onto a

1018456						115 kV power line.  Power was knocked off.

Reportable Incidents - Electrical Equipment:

June 14th	Construction	Windsor		Electrical contact made in a 600 amp panel.  Contact caused a

1020483						transformer to blow.  Event description did not mention any

injuries to workers.

# DATA SUMMARY - Second Quarter

Fatals:		Critical:	Non-criticals:		Powerline	Electrical

Contacts:	Equipment:

2002		    1		      9		          17			       28		         1

2001		    1		    13		          12			       32		         2

2000		    2		      5		          22			       34		         1

1999		    2		      9		          22			       32		         0

1998		    2		      4		          17			       30		         0

Information taken from MIS database - September 5, 2002

Produced by:	Michael Reiser

Engineer

PSS – Kitchener District

Phone:	(519) 883-5682

FAX:	(519) 883-5694

E-Mail:	mike.reiser@mol.gov.on.ca