## Selected Electrical Incidents and Occurrences

Second Quarter - April to June, 2003

Date & 	Program	Location	Accident Description

MIS ID #

Accidents - Fatal:

June 21st		Industrial	St. Thomas	Two sign painters were in the basket of a boom lift.  One

1040932						worker operated the controls in the basket, accidentally moved

the basket towards an overhead 27 kV power line that ran

parallel to the sign.  The second worker was standing in the

corner of the basket closest to the power line, this worker was

fatally injured from contact with the line.

June 26th	Construction	Oakville		Equipment involved was a 600V fused disconnect switch.

1041201						A worker was trying to determine if he could move the one set

of fuse holders in order to get a long fuse to fit.  As he moved

a long fuse about, in the area of the fuse holders, the body of

the fuse bridged between one of the line side fuse clips and

ground.  The arc caused a phase-to-phase-to-phase-to-ground

fault.  The worker received third degree burns to 75% of his

body and died the next day of his injuries.  A second worker

received serious burns to his hands and forearms from the arc.

June 26th	Construction	Selkirk		A farmer was cleaning the eavestrough at his farm.  As he was

1041314						moving a metal ladder, it contacted a 16.8kV overhead line.

The farmer died of his injuries.

Accidents - Critical:

April 10th	Industrial	Toronto		Worker was doing tests on a capacitor bank, did not dissipate

1038321						stored charges in the capacitor after the tests.  When he tried to

disconnect the capacitors, he received a 40 kV shock.  Worker

was taken to hospital.

April 24th	Industrial	Etobicoke	Worker was cleaning around electrical equipment with a wet

1039091						rag.  Received a shock, lost consciousness.

April 25th	Industrial	Barrie		Worker was doing work on a transformer box, touched an

1038711						energized wire, sent to hospital.  Worker received severe burns

to right hand and arm, right thigh and left large toe.

May 2nd		Industrial	Hamilton	Worker was rolling up the welding cable when he received a

1038919						shock and lost consciousness and suffered burns to both

hands.  The single phase machine had been incorrectly connected to the 3 phase power supply, resulting in

the frame becoming energized.

May 7th		Industrial	Brantford	The worker reached into a machine to investigate a source of

1039111						leaking water.  His arm contacted exposed energized terminals

inside the 480 V machine.  Worker lost consciousness,

received burns to his left arm.  Disconnect on the machine was switched off, the terminals were upstream of this disconnect.  The bus plug disconnect switch for this machine, located up high near the ceiling, had not been turned off.

May 17th		Industrial	Mississauga	Worker made contact on a 7 kV conductor, lost consciousness.

1039465						No details given on what work he was doing at the time.

June 17th	Construction	Sudbury		Two workers received severe burns from an electrical arc.

1040757						Workers were working in a meter room at a shopping mall.

Accidents - Non-Critical:

April 2nd		Industrial	Brampton	Flash occurred at a transformer, injured worker taken to

1038013						hospital.  No other details of event given.

April 10th	Industrial	North York	Worker was on a ladder, reached into an electrical box and

1038379						received a shock.  Worker fell off ladder, received a sore back.

April 13th	Industrial	Hamilton	Worker received a shock while pressing a “Door Open”

1038375						pushbutton.  Worker taken to hospital and released.

April 21st	Construction	Nanticoke	Event classified as an electrical contact.

1038656						No other details of event given.

April 23rd	Industrial	Toronto		Worker touched a conduit while plugging in a stereo system.

1038642						Worker complained of a headache and stiff muscles.

April 29th	Mining		Marathon	Worker plugged a drill into a 600 V panel and turned on the

1038972						power.  Event description stated that he touched the feed rail

and received a minor shock.

May 1st		Industrial	St. Thomas	Worker was walking up stairs into the building as lightning

1038873						struck.  Worker’s hand was on the handrail at the time, he was

taken to hospital and released.

May 1st		Industrial	Windsor		While making an electrical connection on 480V equipment,

1039123						the ground wire contacted an energized phase wire.  Worker

was shocked.  (I’m sorry, couldn’t resist)

May 5th		Industrial	Burlington	Worker was using a manlift to get to an overhead crane.

1039242						Worker contacted crane power rails, injury details not given.

May 7th		Industrial	Toronto		Workers were using a ladder to work on eavestrough.  Ladder

1039077						contacted hydro lines; two workers received shocks and were

taken to hospital.

May 11th		Industrial	Peterborough	Worker received a shock from a bun toaster.

1039170

May 14th		Industrial	Scarborough	Worker was cleaning a light from a ladder, received a shock

1039584						and fell off the ladder.  He received minor back injuries.

May 15th		Construction	Pickering	An electrical flash occurred during a test of a 250 VDC set

1039485						of batteries.  Worker was treated for eye flash and returned

to work.

May 22nd	Industrial	Scarborough	Worker received burns from an electrical flash.  No other

1039537						details of event given.

May 27th		Industrial	Peterborough	Worker received a shock from a saucepot.

1039661						Worker was taken to hospital.

May 28th		Mining		Sudbury		Contractor received a shock and was sent to hospital.

1040143						No other details of event given.

June 2nd		Industrial	Thunder Bay	Worker was operating an overhead crane with the pendant

1040369						control.  Worker received a shock, taken to hospital.

June 2nd		Construction	Toronto		Crane struck an electrical wire, wire struck a worker.

1040242						Worker was taken to hospital and released.

June 6th		Industrial	Mississauga	A modified power cable had two male ends.  A worker

1040433						plugged one end into a power source, then began unwinding

the cable to connect to a machine.  The cable arced into his

forearm, worker received a 2nd degree burn.

June 17th	Industrial	Stittsville	Worker was setting up a ladder, wind caught the ladders and

1040858						put it into an overhead line.  Worker received a shock, taken to

hospital.

June 18th	Industrial	Brantford	Worker took hold of an electrical cord, received a shock.

1040827

June 18th	Industrial	Kitchener	Worker doing tree trimming, branch contacted a power line.

1040838						Worker was holding the branch at the time, received a shock.

Worker was taken to hospital.

June 19th	Construction	Espanola	Worker received an electrical shock.  No other details of event

1040891						given.

June 19th	Construction	Mississauga	Worker was using a machine, contacted energized 240V cable.

1041249						Worker taken to hospital.

June 26th	Industrial	Woodbridge	Worker was disconnecting the power supply to a machine,

1041238						the main power switch was not turned off.  Worker received a

shock, taken to hospital.

Reportable Incidents - Powerline Contacts:

April 9th		Construction	Tillsonburg	Event classified as an electrical occurrence at a non-mining

1038237						site.  No other details of event given.

April 9th		Construction	London		Backhoe hit a 12 kV buried cable.  Locates had been done.

1038280

April 11th	Construction	Thunder Bay	Truck contacted overhead power line.  Truck type not

1038338						identified.

April 14th	Construction	Cobourg		Worker was connecting an electrical meter.  Event description

1038418						stated that a power contact was made, but no injuries.

April 17th	Construction	Burlington	Boom of a boom truck contacted an overhead power line.

1038569 & 1039119 (same event)

April 24th	Construction	Toronto		Excavation worker severed a low voltage insulator.

1038732

April 28th	Construction	Dundas		Boom of boom truck contacted a 110 kV overhead line.

1038754

May 5th		Industrial	Sudbury		Crane contacted an overhead power line, two poles were

1038988						knocked down.

May 6th		Construction	Hamilton	Painter put up his ladder, contacted the 240 V service to

1039128						a private residence.  Fuse on transformer blew.

May 6th		Construction	Brantford	Contact made with secondary hydro cables, no other

1040103						information given.

May 8th		Construction	Brighton		Electrical contact made, no other details of event given.

1039131				Township

May 14th		Construction	Bowmanville	Haulage truck hit hydro pole, caused damage to the wires.

1039316

May 14th		Construction	Dundas		Dump truck contacted overhead power line.

1039350

May 15th		Construction	Niagara Falls	Dump truck took down the neutral of a 2.4 kV overhead line.

1039319

May 15th		Construction	St. Jacobs	Dump truck contacted an overhead line.

1039343

May 16th		Construction	Simcoe		While boring, contact was made with a 4 kV buried cable.

1039362						Locates had been done, and boring machine was equipped

with sensors.

May 19th		Industrial	Tiverton		During grading operations, a buried 220 V line was exposed.

1039384

May 21st		Construction	Toronto		While digging for a foundation, contractor made contact with

1039476						a buried cable.

May 29th		Construction	Toronto		Backhoe contacted a 13 kV buried cable.

1040169

June 2nd		Mining		Timmins		Crane contacted an overhead power line.

1040253

June 3rd		Construction	Brampton	Truck contacted a 16 kV overhead line.

1040344

June 3rd		Construction	Leamington	The tarp on a dump truck contacted an overhead

1040355						power line.

June 5th		Construction	Brampton	Worker cut a 27 kV cable, part of the cable fell onto a

1040377						6 kV cable.

June 6th		Construction	Scarborough	Contractor was digging a trench; hit the casing of a power

1040455						line.

June 9th		Construction	London		Paving crew contacted a power line, pulled out a pole.

1040506						No details given of equipment involved.

June 9th		Construction	Beamsville	Backhoe contacted a buried power line.

1040618

June 10th	Mining		Fenelon 		Dump truck hit power line.

1040570				Township

June 10th	Construction	Sioux Lookout	Crane contacted a power line.

1040598

June 12th	Industrial	Brighton		Electrician was repairing a street light, bucket caught on

1040647						an overhead power line.

June 12th	Construction	Mississauga	325 Cat excavator hit a buried 240 V power line.

1041326						Stakeouts had been done.

June 16th	Construction	Hamilton	As a manlift descended, it hit a 600 V power line.  Insulation

1040730						on the power line prevented an electrical hazard, but a lot of

damage was done to the power line where it was attached to

the side of the building.

June 17th	Construction	Cambridge	A truck was dumping asphalt, the raised box contacted an

1040788						overhead power line.

June 17th	Construction	Norwood	Dump truck contacted a power line, caused a breaker to

1040852						trip out.

June 19th	Construction	Windsor		Boom of a shovel contacted an overhead 2400 V power line.

1040928

June 24th	Construction	Kincardine	Hi-Hoe excavator hit a buried line while digging.

1041185

June 25th	Construction	Warkworth	Workers were installing a water main; hit an overhead power

1041145						line with a Hi-Hoe excavator.

June 27th	Construction	Wilmot		Plumber cut into a primary cable.  He also hit a water line and

1041229				Township	caused a flood.

June 27th	Construction	Lakeshore	Dump truck hit a 4800 V line, tore it out.

1041259				Township

June 28th	Construction	Oshawa		Worker struck a buried power line with an excavator.

1041391

# DATA SUMMARY - Second Quarter

Fatals:		Critical:	Non-criticals:		Powerline	Electrical

Contacts:	Equipment:

2003		     3		      7		         25			       39		        0

2002		     1		      9		         17			       28		        1

2001		     1		    13		         12			       32		        2

2000		     2		      5		         22			       34		        1

1999		     2		      9		         22			       32		        0

1998		     2		      4		         17			       30		        0

Report date:	August 7, 2003

Revised:		August 12, 2003 – clarifying information received from Electrical Safety Authority on first and

third fatalities.

Produced by:	Michael Reiser

Engineer

PSS – Kitchener District

Phone:	(519) 883-5682

FAX:	(519) 883-5694

E-Mail:	mike.reiser@mol.gov.on.ca