## Selected Electrical Accidents and Incidents

Third Quarter - July to September, 2001

Date & 	Program	Location	Accident Description

MIS ID #

Accidents - Fatal:

July 13th		Construction	Cambridge	Worker was making a new connection in a 600 V panel, made

1003753						contact with energized section.  Panel had been checked at

start of shift, was not energized.  Disconnect feeding panel not

turned off.  A second crew for another contractor was also

doing work on the main feed, they had previously turned off

the power for their work.  The two crews were not aware of the

work that each other were doing.  When the second crew

turned the power back on, the panel became energized.

August 23rd	Construction	St. Catherines	Linesman doing work on electrical service to a private

1005046						residence.  Worker contacted 110 volts, electrocuted.

Accidents - Critical:

July 24th		Industrial	Guelph		Worker was trouble-shooting an electrically powered overhead

1004020						door.  While on a ladder, fell off ladder due to possible shock.

Worker was not working on the electrics, there was exposed

wiring at the motor.

July 24th		Industrial	Toronto		Worker received burns to both arms and knees from arc.

1004563						Worker was pushing a modular starter cubicle into position in

the MCC when an arc developed at the bus bars behind the

starter.  Starter was OFF as it was being pushed into place.

The area around the MCC was wet, with water dripping from

the ceiling.  There was corrosion in places inside the MCC.

August 9th	Industrial	Toronto		Electrical worker working on energized 600 volt fused

1004605						disconnect switch.  Arc occurred, worker badly burned.

August 14th	Industrial	Weston		Worker received electrical shock from mortising machine.

1004737						Worker lost consciousness.

September 6th	Industrial	Toronto		Worker touched the handle of a portable welding machine

1005521						while also holding onto the rigging of an overhead crane.

Worker received shock, was knocked unconscious.  No

information given on which machine was faulty.

Accidents - Non-Critical:

July 4th		Construction	Newmarket	Electrician contacted 600 volts at a construction site.

1003640						No other details of accident or injuries given.

July 17th		Industrial	Leamington	Millwright lifted an aluminum cast into a heat induction unit.

1005285						Unit was charged with electricity, worker received a shock.

July 19th		Industrial	Toronto		Worker received an electrical shock as he turned on an 18 kW

1004652						light.  Received minor burns to his right hand.

August 1st	Construction	Alliston		Contractor electrician was pulling an energized wire, end of

1000255						wire contacted some metal siding.  Worker received shock,

taken to hospital.

August 2nd	Industrial	Brampton	Transformer exploded, worker was touched by an energized

1004513						600 volt conductor, received burns to hands and neck.

August 7th	Industrial	Longlac		Worker received shock while working on an electrical panel.

1001619						No details given as to type of work being done.

August 7th	Mining		Thunder Bay	Worker doing work in main substation when his hand touched

1001782						a live bus bar.  Worker had locked out the main breaker, did

not know of a tie breaker backfeeding power to the bus.

August 9th	Industrial	Dunnville	Worker reached into a machine, contacted a frayed wire.

1004607						Worker did not lose consciousness, was taken to hospital.

August 10th	Industrial	Cambridge	Student worker bumped against electrical motor, received a

1006141						shock.  No loss of consciousness.

August 14th	Construction	Toronto		Worker received electrical shock from 600 volt equipment.

1004734						Suffered chest pains, did not lose consciousness.

August 15th	Industrial	Leamington	Welder received burns to his fingers from electrical shock.

1007258						Worker had been welding on a boiler.

August 16th	Industrial	Dryden		Worker went to hospital with electrical burns.  No information

1001337						given as to nature of work being done.

August 16th	Industrial	Dunnville	Extension cord was left in water, worker received an electrical

1004741						shock.

August 22nd	Industrial	Etobicoke	Worker received electrical burns to right hand while changing

1005025						a light bulb in an outdoor sign.

August 23rd	Industrial	Jackson’s Point	Worker received electrical shock from a crock-pot, taken to

1005032						hospital then released.

August 25th	Industrial	Mississauga	Electrician made contact while working on electrical

1005091						equipment.  No loss of consciousness, worker still taken to

hospital.  No information given as to nature of work being

done.

September 1st	Industrial	Estaire		Worker was restocking a fridge after it had been repaired.

1005367						Worker received a shock when she put her hand on the top of

the fridge while the door was open.  Worker received entry

burn on right hand, exit wound on side of head.

September 3rd	Industrial	North Bay	Worker was sitting at desk by control panel.  As he went to get

1005795						up, he received an electrical shock.  Hospital reported that

worker had suffered heart palpitations.

September 11th	Industrial	Etobicoke	Worker was using a hand-held rotating polisher.  He received

1005619						an electrical shock from the machine, saw sparks from the

body of the machine.

September 20th	Industrial	Mississauga	Worker turned on the power switch for a grinder.  Machine

1006042						started to spark, worker received burns to arm and hand.

September 24th	Construction	Toronto		Worker for an electrical contractor was connecting services to

1006075						a private residence.  He grabbed the wet wires with his glove,

received a shock, taken to hospital.

September 24th	Construction	Sudbury		Plumber was hooking up a water tank, received a shock.

1006106						Worker taken to hospital.

September 25th	Construction	Stratford		Contact was made with a power line, two workers were injured

1006139						when one of the lines came down.  Line energized at 20 kV.

September 25th	Construction	Nepean		Worker received a shock while using a pole sander

1007310						Worker taken to hospital.

September 27th	Industrial	Brantford	Worker was working on a press, received a 110 volt shock.

1006214						Received a burn to thumb, taken to hospital.

Reportable Incidents - Powerline Contacts:

July 4th		Construction	Ajax		Event classified as a power line contact.

1005782						No other details given.

July 5th		Construction	Peterborough	Event classified as a power line contact.

1005100						No other details given.

July 9th		Construction	Goodson	Event classified as a power line contact.

1001391				Township	No other details given.

July 10th		Construction	Mississauga	Backhoe bucket contacted 16 kV power line while backfilling

1004666						a trench.

July 10th		Construction	Kanata		Boom of a knuckle-type boom truck was extended, contacted

1005524						overhead power lines.

July 11th		Construction	Toronto		Contractor was using a crane to lift material, crane contacted

1005634						power line.  Four tires on truck blew, operator was using a

wireless remote control for the crane.

July 12th		Construction	Ottawa		Backhoe contacted 4800 volt cable.  No information given

1005534						on whether locates had been given.

July 13th		Construction	Brampton	Doing excavating, contacted 27 kV power line.  No other

1003796						details of event given.

July 17th		Construction	Sudbury		Dump truck had a raised box, took out the overhead power

1003816						line.

July 17th		Construction	St. Catherines	Contact made with underground hydro wires, no other details

1004069						given.

July 19th		Mining		Sudbury		Rock drill pulled down a 5 kV power line.

1003957

July 23rd		Construction	St. Catherines	Event classified as a power line contact, no other details

1004397						given.

July 24th		Construction	Sturgeon Falls	Event classified as a power line contact, no other details

1004060						given.

July 24th		Construction	Brampton	Worker for a cable contractor made contact with a buried

1004097						cable.

July 24th		Mining		Sudbury 	Dump truck took down 220 volt power line.  Truck was being

1004210						used to spread slag on a roadway at the time.

July 25th		Construction	Etobicoke	A house was being built, about eight feet from a 4 kV power

1004137						line.

July 26th		Construction	Whitby		A mobile crane contacted a 44 kV overhead power line.

1006942

August 2nd	Construction	Ajax		Dump truck backed into a hydro pole, pole broken.

1006118

August 13th	Construction	Strathroy	Steamroller hit a guy wire of a hydro pole.  The pole broke,

1005330						a pole-mount transformer fell down.

August 14th	Construction	Corbeil		Dump truck hit overhead power line.

1004722

August 15th	Construction	Scarborough	Contractor dug too far, contacted 4 kV power line.

1006553

August 17th	Construction	Mississauga	Dump truck contacted overhead power line.

1004908

August 21st	Construction	Oro-Medonte	Dump truck pulled down a hydro line.

1000114

August 16th	Industrial	Cornwall	Worker trimming trees, small branches touched the power line.

1006756

August 22nd	Construction	Etobicoke	Boom truck contacted the ground wire for a power line.

1004984

August 24th	Industrial	Tilbury		Truck backed into a hydro pole in the company yard, lines fell

1006447						on the truck.

August 27th	Construction	Sudbury		Bucket truck contacted a power line.

1005119

August 28th	Construction	Cambridge	Event classified as a power line contact.  No other details of

1006288						event given.

August 29th	Construction	Guelph		Contractor was using a backhoe, dug into a cable.

1007502						No locates done.

August 31st	Construction	Kanata		Contractor was doing digging, hit a wire.  No information

1007025						given if locates had been done.

September 5th	Construction	St. Joseph Island	Worker was cutting down trees, one tree hit the power line.

1005500						Power knocked out.

September 7th	Construction	Kirkland Lake	Backhoe hit a guy wire, breaking the pole.

1005696						2400 volt line came down.

September 13th	Construction	Toronto		Excavator contacted a high voltage power cable.  Locates had

1006688						been done, workers were to hand dig.  Workers used power

equipment instead.

September 13th	Construction	Ottawa		Boom truck knocked out a power line.

1007399

September 14th	Construction	Peterborough	Backhoe contacted 16 kV power line.  No locates done, they

1007391						were relying on a map.

September 15th	Construction	Etobicoke	Dug up high voltage cable.  No information given on whether

1005939						locates had been done.

September 17th	Construction	Sault Ste Marie	Dump truck contacted the BELL cable with the truck box.

1005801						Pole broken.

September 17th	Construction	Brampton	Worker cut a primary cable.  Cable operating at 27 kV.

1005832

September 17th	Construction	Embro		Dumptruck contacted 4800 volt overhead line.

1006201

September 19th	Construction	Toronto		Worker was using a concrete floor cutter.  Hit a live electrical

1007231						cable.

September 19th	Construction	Huntsville	As a dump truck was moving forwards with box descending,

1007674						lip of box caught on neutral of power line.  Wire broken.

September 19th	Construction	Burlington	Dump truck contacted neutral of power line.

1008127

September 21st	Mining		Matheson	Box of tandem dump truck hit a power line.

1006024

September 25th	Construction	Thunder Bay	Event was classified as a power line contact.  No other details

1001398 & 1001400 (same event)			of event given.

Reportable Incidents - Electrical Equipment:

September 15th	Mining		Bomby		As a worker pushed a START button, breaker cover door blew

1005804				Township	open from a flash.  Breaker was rated for 100 amps, load was a

75 HP fan motor.

# DATA SUMMARY - Third Quarter

Fatals:		Critical:	Non-criticals:		Powerline	Electrical

Contacts:	Equipment:

2001		     2		      5		        25			       44		         1

2000		     2		      5		        26			       42		         0

1999		     3		    11		        24			       40		         0

1998		     5		    13		        13			       40		         2

Information taken from MIS database,  November 28, 2001

Produced by:	Michael Reiser

Engineer

PSS – Kitchener District

Phone:	(519) 883-5682

FAX:	(519) 883-5694

E-Mail:	mike.reiser@mol.gov.on.ca