## Selected Electrical Accidents and Incidents

Third Quarter - July to September, 2002

Date & 	Program	Location		Accident Description

MIS ID #

Accidents - Fatal:

August 23rd	Industrial	North York	Worker received a fatal electrical shock while changing the

1027843						ballast in a fluorescent light fixture.  Voltage of light fixture

was 347 volts.

Accidents - Critical:

July 2nd		Industrial	London		Two workers were involved in an electrical arc incident.  First

1018374						worker was checking connections at the connection box for a

fan when an arc occurred.  First worker received major burns,

the second worker was treated at the scene.

July 4th		Construction	London		Linesman was working on overhead lines when he contacted a

1018466 & 1032478 (same event)			120 volt circuit.  Worker climbed down the pole to catch his

breath, lost consciousness as he was sitting at a table on the

ground.

July 9th		Industrial	Toronto		Worker doing work on electrical wiring in ceiling of office.

1020418						Electrical contact made, worker lost consciousness.

July 19th		Industrial	Durham		Electrician had locked out the power to the splitter he was

1023301						about to work on.  Splitter was still energized, arc caused

burns to face, arms and hands.  Worker was actually working

on a different splitter from the one that he had locked out.

Employer will improve labeling of electrical equipment.

July 20th		Industrial	Mississauga	Worker received an electrical shock while working on a

1022647						microwave tower, voltage unknown.  Worker’s heartbeat

became irregular.

July 23rd		Construction	London		Worker (non-electrician) drilled into a 600 V bus duct to use

1023270 & 1026073 (same event)			the enclosure as a support for a light fixture.

Electrical explosion occurred, worker received severe burns.

July 29th		Construction	London		Electrician received a shock while working off a ladder.

1032724						Worker fell to the ground, lost consciousness.

July 31st		Construction	Etobicoke	Worker was chipping concrete, contacted 347 volt power line

1023660						in conduit.  Worker was knocked unconscious.

September 5th	Industrial	Oakville		Electrician was in the process of replacing some wiring in a

1030364						MCC.  As the cable was being moved, it brushed against a

ground wire.  The ground wire became unattached and

contacted the bottom of one of the bus bars.  The resulting

arc caused major burns to the worker’s right hand and arm.

September 23rd	Industrial	Mississauga	Event description stated that an electrician received 3rd degree

1031237						burns to his hands.  No other details given.

Accidents - Non-Critical:

July 2nd		Industrial	Chatham		Worker received a shock while putting parts in a metal bin.

1028249 & 1023591 (same event)			An electrical cord under the bin had been damaged, a bare

wire was touching the bin.

July 3rd		Construction	Aylmer		Two workers were involved in an electrical contact incident,

1031040						both workers taken to hospital.  No other details given.

July 5th		Industrial	Brampton	Owner of business doing electrical work.  Arc occurred,

1019765						received burns to hands and face.  No other details given.

July 9th		Industrial	Toronto		Worker doing trouble-shooting on lighting circuit.  Contact

1032556						made, worker received burns to a finger and the palm of his

right hand.

July 15th		Industrial	Long Sault	Worker received a shock as he was plugging a heater into a

1020970						die machine.  Arm felt numb, no burns, worker did not lose

consciousness.  No information given on source of electricity.

July 17th		Construction	Woodbridge	Worker was painting mouldings beside an electrical room.

1021099						An electrical explosion occurred, worker received minor burns

to about 10% of his body.

July 22nd		Construction	Welland		Worker received an electrical shock from a faulty electrical

1026023						impact wrench.

July 22nd		Construction	Mississauga	Worker received a shock from the welding machine.  Machine

1024168						was wet from rain at the time.

July 24th		Industrial	Windsor		Worker became caught up in a spot welder machine as it

1025594						cycled.  Worker received an electrical shock as the welder did

the spot welding operation.

July 25th		Construction	London		Worker laid a chainsaw across a cable, a fixed tooth on the

1032718						chainsaw housing punctured the cable insulation.

Arc occurred, worker received minor burns.

July 29th		Industrial	Ajax		Worker received 3rd degree burns from an electrical contact.

1023524						Event classified as non-critical, no other details given.

July 29th		Industrial 	Arnprior		Worker touched electrical wires, received an electrical shock

1027191						and fell about ten feet off the ladder.

August 2nd	Industrial	Nepean		Worker received a shock from a faulty power bar.  Worker had

1023877						wet feet and hands as he was unplugging the unit.

August 6th	Industrial	Toronto		Worker received an electrical shock while working on a

1030843						machine while the power was still on.  Received 2nd degree

burns to right hand.

August 7th	Construction	Ottawa		Worker received an electrical shock while drilling off a

1024128						scaffold.

August 12th	Construction	Streets-Ville	Crane contacted an overhead line, worker taken to hospital.

1025622

August 12th	Industrial	Brampton	Worker received an electrical shock while working in a

1025812						kitchen.  Worker was taken to hospital, treated and released.

Event description did not specify what equipment was

involved.

August 13th	Construction	Mississauga	Worker was lowering a scissorlift, got caught up in an

1025828						electrical tray.  Worker received shock from 347 V.

August 13th	Mining		Timmins		Workers doing planned maintenance, arc developed between

1026156						bus bars and a sling.  One worker received minor injuries.

August 14th	Industrial	Shelbourne	Event description states that worker received a static shock.

1026064						Worker had trouble breathing and was vomiting.

Worker was taken to hospital.

August 14th	Industrial	London		Forklift truck hit a light fixture.  Worker tried to move light,

1026150						received an electrical shock and fell about 20 feet.

August 14th	Construction	Stoney Creek	Worker doing hand shoveling around a buried cable, shovel

1027681						nicked the insulation.  Worker felt a tingle.

August 15th	Construction	Barrie		Worker using excavator, contacted a buried cable.  Worker

1026032						sent to hospital with pains in his arms.

August 16th	Industrial	Rexdale		Worker received a shock while unplugging an electrical cord.

1026096						Event details stated that she touched a wire in the plug.

August 17th	Industrial	Hamilton	Electrician was doing trouble-shooting on a 2300 V panel.

1026127						Made an electrical contact, received burns to hands and

forehead.

August 22nd	Industrial	Kingston	Worker was changing a light fixture using an aluminum ladder.

1027838						Received a shock, fell from ladder.  Received severe bruising

to legs, no electrical burns.

September 9th	Industrial	Tiverton		Worker received a 120 volt shock from a power tool.  The

1030562						GFCI had tripped, the worker told his helper to go and reset

breaker.  The worker continued to hold onto the drill while the

breaker was being reset.  Worker taken to hospital and

released.

September 10th	Construction	Etobicoke	Worker received a shock from an energized wire.  No details

1030637						given as to work being done at the time.

September 10th	Construction	Toronto		Worker made contact with an energized wire.  Worker

1030922						contacted wire before electrician had locked it out.  Worker

received minor burns.

September 12th	`Construction	Stoney Creek	Workers were using high-pressure water to excavate down to a

1030778						faulted 16 kV buried cable.  A bad splice in a second

energized cable was penetrated by the water, worker received

a shock through the metal wand.

September 12th	Construction	Toronto		Worker was injured from an electrical contact.  No other

1030973						details given.

September 16th	Industrial	Kitchener	Worker was doing work on a machine when he received a

1030934						shock.  Worker taken to hospital, no other details given.

September 17th	Construction	London		Electrician received a shock while working off a ladder.  Event

1030985						description did not specify what work the worker was doing.

September 26th	Construction	Brantford	Boom of crane contacted 24 kV overhead lines, one worker

1031412						reported tingling in his hand.  Event description did not

specify where the worker was at the time the crane made

contact.

Reportable Incidents - Powerline Contacts:

July 4th		Construction	Mississauga	Electrical contact made with buried cable.  Stake out had

1030889						been made.

July 5th		Construction	Hamilton	While torpedoing across the street, the contractor hit a

1030752						4 kV buried cable.

July 10th		Mining		Longlac		Flyrock from a blast damaged some hydro poles.

1020927

July 11th		Construction	Tiverton		Event classified as a power line contact.  No other details

1027650						given.

July 12th		Construction	Brampton	A buried line was cut.  Cable voltage was 27.6 kV.

1020881

July 16th		Construction	Barrie		Hydro contact, no other details given.

1020974

July 17th		Construction	Hamilton	Workers were excavating a hole for a pole using a

1023369						jackhammer.  Contacted a 13 kV buried cable.

July 18th		Construction	Dover Township	Excavator dug up a 4800 V buried cable.  No locates

1027590						had been done.

July 24th		Construction	Collingwood	Contact made with 4800 volt line.  No other details

1023339						given.

July 26th		Industrial	Dunnville	Crop sprayer contacted a 4800 volt line.

1023542

July 26th		Construction	Toronto		Electrical contact on a 2400 volt cable, no other details given.

1027980

July 29th		Construction	Brant County	Grading road, contacted and pulled down the neutral of an

1023541						overhead line.

July 30th		Construction	Toronto		Electrical contact made while replacing water services.

1023577						No other details given.

July 30th		Construction	St. Catherines	Boom truck contacted power lines while traveling on a

1031066						residential street.  Power lines severed.

July 31st		Industrial	Woodbridge	Boom truck contacted overhead line.

1023627

August 1st	Construction	Waterford	Dump truck contacted overhead hydro line.

1023732

August 2nd	Construction	Concord		Crane contacted 8 kV power line.

1023814

August 2nd	Construction	Welland		Worker contacted 600 V cable, no other details of event given.

1031071

August 7th	Construction	Markham	Excavator contacted a buried cable.

1024169

August 7th	Industrial	Vaughan		Tractor trailer contacted hydro line.

1024172

August 7th	Construction	Vaughan		Excavating work, contacted buried cable.

1024184

August 8th	Construction	Kapuskasing	Dump truck contacted the hydro line.

1025568

August 9th	Industrial	Cambridge	Truck with crane attachment was moving while the crane was

1025836						elevated.  Contacted a 240 V overhead line.

August 12th	Construction	Stoney Creek	Event classified as electrical, no other information given.

1025818

August 12th	Construction	Dundas		Event classified as powerline contact, no other details given.

1027675

August 14th	Construction	Wellington	Dump truck hit overhead wires.  Power knocked off.

1025895

August 14th	Construction	Kanata		Workers were transporting pipe, contacted overhead lines.

1025966

August 15th	Construction	Smooth Rock	Truck driver backed into hydro pole.

1026029				Falls

August 15th	Construction	Trout Creek	Dump truck drove forwards with the box in the raised

1026930						position.  Overhead lines contacted.

August 15th	Industrial	Hamilton	Electrical contact made.  No other information given.

1027678

August 16th	Construction	Madoc		Backhoe contacted overhead power lines while doing

1026066				Township	digging at a private residence.

August 16th	Construction	Toronto		Mobile crane contacted overhead lines.

1026072

August 20th	Mining		Manitoulin	Contractor was doing some blasting.  Flyrock hit a conductor

1026349				Island		in a substation, substation was knocked off-line.

August 20th	Construction	Hamilton	Backhoe contacted buried 240 V electrical cable.

1027569

August 20th	Construction	Thunder Bay	Dump truck drove away before the box was completely

1027620						lowered.  Box lip caught telephone line, caused pole to snap.

Pole also supported a 25 kV line.

August 20th	Construction	Hamilton	Dump truck contacted a 27.6 kV line inside a substation while

1027870						dumping a load of gravel.

August 21st	Construction	Guelph		Dump truck hit an overhead line.

1027593

August 21st	Construction	Whitby		Contact made with buried street lighting circuit.  Equipment

1027624						involved not specified.

August 21st	Construction	Blenheim	Event classified as electrical, no other details given.

1027677

August 22nd	Construction	Thunder Bay	Dump truck contacted high voltage power line.

1027688

August 29th	Construction	Timmins		Bulldozer pulled on a 600 V conductor while backfilling

1029116						a trench.

September 4th	Construction	Leamington	While lifting the broken lid of a vault, a piece of rebar flipped

1030310						and punctured a cable.

September 6th	Construction	Glen Robertson	Excavator was moving from one location to another,

1030425						counterweight hit a pole of an overhead line.  Utility was

on site and immediately had line de-energized.

September 6th	Construction	Etobicoke	Crane contacted a 16 kV overhead line.

1030439

September 9th	Construction	Peterborough	Event classified as electrical, no other details given.

1030450

September 9th	Construction	Vaughan		Contractor dug into a series of high voltage cables.

1030542						No stakes put out.

September 9th	Mining		Longlac		Flyrock from a blast damaged overhead power line in the area.

1030801

September 11th	Construction	Paris		Dump truck contacted the neutral of an overhead power line.

1030753

September 13th	Construction	Renfrew		Truck hit hydro pole, two poles knocked down.

1030827

September 14th	Construction	Balmertown	Crane contacted overhead power line.

1031200

September 16th	Construction	Thunder Bay	Contractor contacted a buried 25 kV cable during digging

1031008						operations.

September 17th	Construction	Burford		Contact made with overhead power line.  No other details

1031060						of event given.

September 17th	Construction	St. Catherines	Backhoe contacted 8 kV buried cable.

1031131

September 18th	Construction	Hamilton	Jackhammer Bobcat contacted a buried primary cable.

1031131

September 19th	Construction	Picton		Backhoe contacted overhead power line.

1031168

September 19th	Construction	Toronto		Crane contacted overhead 27kVpower lines.

1031298

September 23rd	Construction	Essex County	Concrete truck contacted 4800 V overhead power lines.

1031461

September 26th	Construction	Milton		Contact made with overhead power lines.  Conveyor style

1031615						boom was left elevated as equipment was driven away.

September 27th	Construction	Guelph		Contact made with 240 V overhead residential service.

1031531						No details given of equipment that made the contact.

# DATA SUMMARY - Third Quarter

Fatals:		Criticals:	Non-criticals:		Powerline	Electrical

Contacts:	Equipment:

2002		     1		     10		        34			       59		        0

2001		     2		       5		        25			       44		        1

2000		     2		       5		        26			       42		        0

1999		     3		     11		        24			       40		        0

1998		     5		     13		        13			       40		        2

Information taken from MIS database,  December 5, 2002

Produced by:	Michael Reiser

Engineer

PSS – Kitchener District

Phone:	(519) 883-5682

FAX:	(519) 883-5694

E-Mail:	mike.reiser@mol.gov.on.ca