## Selected Electrical Incidents and Occurrences

Third Quarter - July to September, 2003

Date & 	Program	Location	Accident Description

MIS ID #

Accidents - Fatal:

July 4th		Industrial	Richmond Hill	Worker was doing electrical work in a private residence,

1041488						made contact with an energized conductor.

July 5th		Construction	Bruce Mines	Worker was involved in replacing overhead lines when he

1041493						made contact with a 7200 V phase.  Worker was working from

bucket of an elevating work platform at the time.

July 24th		Industrial	Wasaga Beach	A non-worker was doing plumbing work at his trailer in a

1042323						trailer park when he made electrical contact and was killed.  An examination of the trailer’s electrical system after the fatality noted that the trailer’s ground connection was defective, and that the power and neutral leads in one of the circuits had been 	reversed.

August 15th	Construction	Tiny Township	A shingling worker was removing roof jacks when a gust of

1043354						wind blew his ladder into 2400 V power lines.  The worker

collapsed and died from the contact.

August 25th	Construction	Norwich		A worker was dumping a load of gravel at a road construction

1043004						site.  The worker started the box in motion to raise it, then

stepped out of the truck while the box was being raised.  The

driver noticed the power lines, went back to the truck to try to

stop the box’s motion before it hit the lines.  The worker

grabbed hold of the boarding handle beside the door while his

feet were still on the ground.  The worker dropped to the ground, was pronounced dead at the scene.  Operating voltage of the lines was 4800 volts.

Accidents - Critical:

July 2nd		Construction	Primrose	Worker was doing shingling work on a display cottage.

1041358 & 1041571 (same event)			His head contacted a 4800 V power line above the roof area.

July 30th		Industrial	Sarnia		Worker contacted 347 V, fell off the ladder and lost

1042533						consciousness.  Worker was treated by paramedics and

returned to work.

August 6th	Construction	Etobicoke	A scaffold was in contact with a 27.6 kV power line.

1042667						A worker touched the scaffold to begin to climb it.

The worker collapsed and was taken to hospital

August 7th	Construction	Ottawa		Two workers were nailing a bell fitting around a live

1042724						conductor, operating at 13.8 kV.  A nail punctured the cable,

contacting a live conductor.  Both workers received electrical

contact injuries, one of the workers was also burned from entry

and exit wounds.

September 22nd	Industrial	Oakville		Worker unscrewed front cover plate of a 600V transformer,

1044199						then reached into the transformer with her bare arm.

Transformer was still energized, labels were in place, and the

breaker for the transformer was in the panel above it.

Worker’s lower arm and hand were severely burned.

September 23rd	Construction	Caledonia	Worker was setting up a speaker on top of a transformer,

1044272						contacted 4800 V, fell about 20 feet to the ground.  No details

given of injuries suffered.

Accidents - Non-Critical:

July 3rd		Industrial	Innisfil		Worker was trimming trees below a power line, received

1041603						tingling in his fingers.

July 4th		Industrial	Timmins		Worker was struck by lightning, lost his vision for a few

1042092						seconds.

July 7th		Construction	Iroquois Falls	Worker was doing cutting with a torch when he cut into

1041537						a 12 kV conductor.  Worker was taken to hospital with burns.

Cables shown on the blueprint had been de-energized, but

the  prints did not show this cable.

July 10th		Mining		Hemlo		Worker was feeding a cable into a connector for a fan starter.

1041811						A second worker turned on the fan’s control switch.  When the

starter closed, the electrical flash blew out through the

connector and burned the worker’s hand.

July 11th		Construction	Pembroke	Worker was doing work on an electrical panel when he

1041716						received flash burns to his face and hands.

July 16th		Industrial	Toronto		Worker did not turn off the power before beginning work,

1041919						caused a short.  Received 2nd degree burns to right arm.

July 18th		Construction	Toronto		Worker made contact with a live conductor, received a tingle

1042696						but no other obvious injuries.

July 19th		Industrial	Oshawa		Worker received a shock when she touched some old wiring

1042339						attached to a hotplate.

July 30th		Construction	Mississauga	Worker was installing light fixtures, received a 347 V shock to

1042494 & 1042523 (same event)			his left hand.  Worker was taken to hospital.

July 30th		Construction	Harley		A young worker was using a metal rod to probe the ground to

1042519						look for a buried electrical cable.  During one of the probes,

the rod went through the conduit and cable jacket, contacting a

power phase for the 600 V cable.  The worker received an

electrical shock and was taken to hospital.  The crew knew

there was a buried cable in the area, and were hand digging the

foundation trenches, but had not found the exact location of

the cable at the time.

July 30th		Construction	Toronto		Worker was trying to put in a new light, received shock from

1042559						347 volts.

August 1st	Industrial	Peterborough	Two workers were cutting down a tree, dropped it onto a

1042592						power line.  One of the workers was touching an aluminum

ladder with his forearm, received burns to the forearm.

August 6th	Industrial	Oshawa		The worker was cleaning an electric stove when he felt a

1043292						shock, was taken to hospital.

August 8th	Construction	Mississauga	Worker was driving steel posts, felt a tingle.  Post was tested,

1042758						found to be energized.

August 16th	Industrial	Windsor		Worker received an electrical shock, no details given of work

1043044						being done at the time.

September 6th	Industrial	Brampton	Worker made contact with 480 volts, received a burn to the

1043611						little finger on left hand.  No details given of work being done.

September 6th	Industrial	Maple		Worker made electrical contact while changing a fluorescent

1043619						tube in a sign.  Taken to hospital then released.

September 10th	Industrial	Toronto		Workers received shocks from a milk shake machine.

1043868						One worker sent to hospital and released.

September 11th	Industrial	London		Worker received an electrical shock from a dishwasher, taken

1043855						to hospital and released.

September 15th	Construction	North York	Electrical contractor was working on a panel, received an

1043895						electrical shock.  Worker taken to hospital then released.

September 17th	Industrial	L’Original	Event description states that a worker received burns to face

1044068						and right arm from an electrical contact.  No other details of

event given.

September 24th	Construction	Scarborough	Electrical contractor working on electrical fixture, contacted a

1044367						live wire.  Received burns to right hand and left fingertip.

September 25th	Construction	Nepean		Worker hit by lightning, received minor burns to toes.

1044345

September 25th	Industrial	Breslau		Leads from a welding machine were not properly attached to

1044368						work piece, another worker received an electrical shock.

Reportable Incidents - Powerline Contacts:

July 2nd		Construction	Lakefield	Swing-hoe contacted the neutral of an overhead line.

1041335

July 2nd		Industrial	Kingston	Dump truck was traveling with the box raised, caught the

1041375						telephone cable.  Two poles knocked down.

July 3rd		Construction	Vaughan		Gravel truck hit a power line, snapped off one pole.

1041382

July 5th		Construction	Hearst		While disassembling a crane just outside a substation, a load

1042194						line contacted a 14.4 kV conductor.  Conductor was burnt off.

July 7th		Construction	Toronto		A crane touched overhead lines, knocking off the circuit.

1041556

July 8th		Industrial	Ear Falls		Equipment on a low-bed trailer contacted 115 kV power line.

1041602 & 1041740 (same event)

July 8th		Construction	Sudbury		The raised box of a dump truck broke the neutral wire of an

1041666						The truck had dumped its load and was pulling away, the

driver ignored the signals from a signaler present at the scene.

July 11th		Construction	Hill Island	Equipment on a float got caught on the telephone line,

1041708						knocked down one pole.

July 12th		Mining		Longlac		Flyrock from a blast damaged a transmission line and the

1041901						telephone cable.

July 14th		Construction	Espanola	Contractor hit a buried cable, no details given of equipment

1041750						involved.

July 14th		Construction	Fraserville	Hydro contact, no other details given.

1041786

July 15th		Construction	Vaughan		Contact made with a 16kV power line, no other details given.

1041841

July 17th		Industrial	Leamington	Tree service was removing a limb from a tree, limb broke the

1042032						2400 V overhead line.

July 22nd		Construction	St. Catherines	Bucket truck contacted the primary of an overhead line.

1042197

July 24th		Mining		Mara Township	A crane was hoisting equipment onto a flatbed trailer, made

1042319						contact with a 44 kV overhead line.

July 24th		Construction	London		Contractor put an auger through a 1600 V buried cable.

1042330

July 28th		Construction	Burlington	Excavator contacted the neutral of an overhead line.

1042424

July 28th		Construction	Concord		Contractor was digging, contacted buried 27.6 kV power line.

1042442

July 28th		Construction	Malton		High-hoe excavator contacted an overhead service line.

1042521

July 31st		Construction	Vaughan		Contact made with a buried 27.6 kV cable.  No other details

1042659						given.

July 31st		Construction	Bowmanville	Crew was removing a pole transformer when the boom tip of a

1042797						radial boom derrick contacted a 4800 V overhead conductor.

August 1st	Construction	Espanola	Contractor pushed a tree into a 2400 V power line.

1042608

August 5th	Construction	Dryden		While digging, workers uncovered a buried electrical cable.

1042835						The pole transformer tripped off the power.

August 6th	Construction	Vaughan		Event classified as a power line contact.

1042718						No other details of event given.

August 8th	Construction	Toronto		A scaffold contacted a 4 kV power line.

1042790

August 11th	Industrial	LaSalle		A tree trimming operation dropped a tree on a 16 kV power

1042905						line.

August 11th	Construction	King Township	Event description mentioned poles and lines.

1042912						No other details of event given.

August 14th	Construction	Thunder Bay	Two workers dug up a 25 kV buried cable.

1043037						No locates had been done.

August 18th	Construction	Aurora		Bucket of a backhoe contacted a buried 8 kV power line.

1043072						Locates had been done.

August 20th	Construction	St. Catherines	Backhoe nicked a primary cable, caused power outage in the

1042996						neighbourhood.

August 20th	Construction	North Augusta	Operator was moving an excavator, contacted a 48 kV

1043045 & 1043688 (same event)			overhead line.

August 21st	Construction	Mississauga	Worker was using a bar in digging a ditch, hit a power line.

1043090

August 22nd	Construction	St. Catherines	Auger machine contacted a buried cable.

1042995						Cable voltage given as 8 kV.

August 26th	Construction	Sarnia		Front end loader contacted an overhead power line.

1043908

August 28th	Construction	Brampton	Backhoe hit the neutral of an overhead power line.

1043287

September 2nd	Construction	Scarborough	A Hi-Lo excavator hit the overhead wires.

1043353

September 3rd	Construction	Kingston	Event classified as electrical occurrence, no other details

1043641						given.

September 4th	Construction	Stouffville	Excavator made contact with a 4800 V buried cable.

1043498

September 4th	Construction	Guelph		325 Cat excavator contacted a buried secondary power line.

1043683

September 8th	Construction	King City	Electrical contact made with overhead lines, no details given

1043631						of equipment involved.

September 10th	Construction	North York	Backhoe being used to expose the ends of a new hydro duct.

1043832						Bucket skinned a primary cable.

September 11th	Construction	Brampton	Contractor cut a buried 27 kV power line.  No guide markings

1043807						on the ground.

September 15th	Industrial	King Township	Event classified as power line contact, no other details given.

1043914

September 15th	Industrial	St Joseph Island	Crew clearing power line, tree brushed against a 14.4 kV line.

1043936

September 16th	Construction	Blind River	Excavator contacted a buried power line.

1044026

September 16th	Construction	Massey		Excavator severed a 240 V power line.

1044106

September 17th	Construction	Thunder Bay	Worker digging, contacted a buried 25 kV cable.

1044029

September 23rd	Construction	Waterloo	Digging, contacted a buried primary power line.

1044246						No locates.

September 27th	Construction	Toronto		Event description states “electrical contact with equipment”.

1044792						Event classified as an occurrence, no other details given.

September 29th	Construction	Thunder Bay	Contractor cutting trees, dropped one on a 25 kV circuit.

1044662

Reportable Incidents - Electrical Equipment:

August 8th	Industrial	Etobicoke	Worker tried to operate the handle of a breaker, when he

1042991						couldn’t, he got out a screwdriver.  The inevitable happened,

the breaker shorted to ground, fortunately no injuries.

August 12th	Mining		Marathon	Flyrock from a blast underground damaged an electrical panel.

1043551

September 3rd	Construction	Guelph		Forklift went through the side of a padmount transformer.

1044900

September 30th	Mining		Sudbury		Bucket of Bobcat cut a battery in half.  Battery caught on fire.

1044809

# DATA SUMMARY - Third Quarter

Fatals:		Critical:	Non-criticals:		Powerline	Electrical

Contacts:	Equipment:

2003		     5		      6		        24			       50		        4

2002		     1		    10		        43			       59		        0

2001		     2		      5		        25			       44		        1

2000		     2		      5		        26			       42		        0

1999		     3		    11		        24			       40		        0

1998		     5		    13		        13			       40		        2

Information taken from Ministry of Labour MIS database

Assembled by:	Michael Reiser

Engineer

PSS – Kitchener District

Phone:	(519) 883-5682

FAX:	(519) 883-5694

E-Mail:	mike.reiser@mol.gov.on.ca