## Selected Electrical Accidents and Incidents

Fourth Quarter – October to December, 2001

Date & 	Program	Location	Accident Description

MIS ID #

Accidents - Fatal:

October 2nd	Industrial	North York	Non-worker was helping to trim trees at a private residence.

1006349						Victim was sawing off a branch when it came down on a high-

voltage power line.  Victim received an electrical shock, died.

No information given as to voltage of power line.

October 26th	Construction	Belleville	Double Fatality.  Crane was being moved backwards along

1003240 & 1007148 – Same event			the median of a highway while the crane boom was raised.

Boom of crane contacted bottom phase of a 44 kV line running

across the highway.  One worker was acting as a signaler for the driver of the crane, this worker went back to the crane when the boom made contact.  Worker touched body of crane while standing on the ground, worker died.  Second worker was driving the crane from the crane’s truck cab.  This worker got out to see what happened to the first worker, was in contact with the crane and the ground at the same time, worker also died.

November 1st	Construction	Cambridge	Worker was electrocuted as he disconnected a 30 amp 600 volt

1007364 & 1008263 – same event			pin and sleeve connection.  An earlier electrical incident had

led to the ground wire and metal casing of the flexible cable to

become energized at 347 volts to ground.  As the worker broke

the connection, the current flowing through the ground wire

flowed through the worker’s body.  The investigation after the

accident found a spot, where the metal conductor of one of the

phases on the line side was touching the metal of the conduit

going into the disconnect switch for the flexible cable.  This

point of contact was downstream of where the regular ground

connection had been broken as a result of the earlier incident.

December 4th	Construction	White Lake	Two workers were installing de-icing cables on a roof.  As

1008314						they were moving a ladder from one part of the roof to

another part, the ladder touched an overhead line.  Both

workers were knocked down, one of the workers was killed

by the contact.

Accidents - Critical:

October 10th	Industrial	North Bay	Electrical contact made, current path was through one arm and

1006597						out the other.  No other details given.

October 11th	Construction	Toronto		Two workers, non-electricians, were injured when an

1006615						explosion occurred in a transformer building.  A metal tape

being used by one of the workers caused a 115 kV arc to

ground.  One worker received burns to his face and body, the

other received flash burns to his eyes.

October 12th	Mining		Lively		Electrician was checking fuses on a 600 V panel.  Electrical

1006639						flash occurred, worker was burnt to his face and hand.  Event

details did not mention the model of multimeter in use.

October 30th	Industrial	Rexdale		Painting contractor suffered burns, knocked unconscious from

1007298						contacting 16 kV transformer.

October 30th	Mining		Timmins		Worker was boosting a vehicle; one of the batteries blew up.

1007299						Worker jumped out of the way and fell.  Worker was knocked

unconscious by the fall.

November 1st	Industrial	Sudbury		Worker was removing material from around some signs,

1007376						accidentally touched the caging around one of the signs.

Worker received a shock, lost consciousness.

November 5th	Industrial	Huron County	Truck driver was dumping corn out of the truck box, as the

1007473						box was raised, it contacted a hydro line.  The driver went

back to the truck to lower the box, received a shock as he

touched the truck.  He received burns to his hands and feet.

November 7th	Industrial	St. Catherines	Linesman contacted an energized overhead conductor,

1007826						received 2nd and 3rd degree burns to his face and neck.

No information given as to work being done at time of event.

December 5th	Construction	Leamington	Worker was guiding a steel joist into position when the joist

1008315						contacted a 16 kV overhead line and became energized.

Worker received a shock, fell about 25 feet to the ground.

Worker had burns to his hand and arm from the electrical

contact, as well as a broken hip and leg injuries from the fall.

Accidents - Non-Critical:

October 9th	Construction	Toronto		Worker was feeding BX cable through a hole in the floor of an

1007129						apartment into a hydro vault.  The cable contacted a 16 kV bus

bar in the vault, worker received a burn mark to his hand and

an exit wound on his knee.

October 10th	Industrial	Toronto		Worker was inserting a BX cable into a junction box.

1007614						A Marrette connector fell off, a wire touched a grounded wire.

A shock injured fingers on his left and right hands.

October 12th	Industrial	Stoney Creek	Worker received an electrical shock, left hand and wrist were

1008396						swollen.  No details given of work being done or equipment

involved.

October 16th	Industrial	South Sandwich	Worker plugged a cord into a power outlet.  As he touched the

1009735				Township	plug, he received a shock, had a burn on his hand.

October 17th	Construction	Mississauga	Worker was installing a power meter.  A meter tool contacted

1006874						the electrical box, flash occurred.  Worker had third degree

burns to hands, partial burns to face.

October 18th	Industrial	Kitchener	Electrician received a shock while making an adjustment on a

1009616						flex cell packer.  Current was enough to burn off the band of

his wrist watch.

October 20th	Construction	Nanticoke	Worker hooking up air connection to plasma machine when he

1007184						received a 347 volt shock.  No other injuries reported.

October 22nd	Industrial	North Bay	Battery blew up, two workers received acid in their faces.  No

1006955						details given as to work being done at the time.

October 24th	Industrial	Woodbridge	Worker cleaning bag sealer machine, received an electrical

1007076						shock.

October 24th	Industrial	Huntsville	Millwright was checking fuses in an energized fuse box.  Flash

1009711						occurred, worker was burned to hands and one arm.  Company

policy was to have fuse boxes locked out before checking

fuses.

October 28th	Industrial	Welland		Worker contacted hydro lines, fell about 20 feet.  No other

1007756						details of accident given.

October 29th	Construction	Brampton	Elevator was being installed, electrician turned on the power to

1007220						do some checking.  He crossed some wires and received a 600

volt shock.

November 1st	Industrial	Pickering	Worker received an electrical shock while cleaning an

1008345						electrical panel.  No other details of the incident given.

November 2nd	Industrial	Gloucester	Worker was doing electrical work on a sign when he received

1008909						an electrical shock.  No other details given.

November 7th	Industrial	Spruce Falls 	Worker suffered electrical burns to his right hand while he was

1008203						changing a light fixture.  Fixture was operating at 347 volts.

November 13th	Industrial	Guelph		Electrical worker was disconnecting a lead from a transformer

1008507						under test.  Transformer was still energized at the time, worker

received a shock, was knocked down.

November 16th	Mining		Copper Cliff	Electrician received electrical flash to his eyes as he was

1007850						racking in a 600 volt breaker.  Cause thought to be faulty

wiring in the breaker.

November 16th	Construction	Carleton Place	Electrician received 347 volt shock as he was installing a

1009742						ceiling heater.  Worker received nerve damage to right hand.

November 20th	Industrial	Toronto		Worker was changing lights while standing on the back of a

1007923						truck.  Received a shock and fell off the back of the truck.

November 23rd	Construction	Nepean		8 kV electrical circuit knocked down a worker.  No details

1009674						given as to work being done at the time of the accident.

November 28th	Construction	Ottawa		Worker contacted 1500 volt overhead line with a ladder.

1010115						No details given as to injuries received or what work was

being done at the time.

November 30th	Industrial	Mississauga	Worker was working on an electrical box, touched an outside

1008210						wire, box exploded.  Victim was knocked over, has burn marks

on his lab coat.

December 4th	Construction	Markham	Electrician received a shock from a live electrical circuit.  No

1008279						other details of accident given.

December 5th	Mining		Timmins		Two workers received minor burns when they disconnected a

1009019						live 4160 volt trailing cable.

December 10th	Industrial	Blyth		Two workers were injured while using a meter to check fuses.

1008467						One worker was holding the meter while the other was holding

the probes.  Both workers received an electrical shock as the

probes touched the fuses.  No information was given on the

make and model of the meter.

December 11th	Construction	Mississauga	Worker drilled into a hydro pole, received a shock.  Worker

1008509						was employed by a communications company at the time.

December 11th	Industrial	Toronto		Electrician was opening a switch box, flash occurred.  Worker

1009783						received burns to face and neck.

December 13th	Construction	Mississauga	Welder was standing in a puddle of water when he turned on a

1008585						welding machine.  Received a shock, taken to hospital.

Reportable Incidents - Powerline Contacts:

October 1st	Construction	Geraldton	Raised box of a dump truck contacted an overhead line.

1001456

October 1st	Construction	Atikokan	Backhoe struck a utility pole.

1001520

October 1st	Construction	Playfair		Contractor dropped a tree on a 7200 volt overhead line.

1006319				Township

October 2nd	Construction	Brampton	Contractor doing directional drilling, hit a 2700 volt cable.

1006372						No locates done.

October 2nd	Construction	Toronto		Contractor contacted a buried cable.

1007941						No information given as to equipment involved.

October 3rd	Construction	Holland Landing	Equipment contacted 44 kV line.  No information given as to

1000118						type of equipment involved.

October 3rd	Construction	Brampton	Event description said a conveyor was touching a 44 kV

1006402						overhead line.  Contractor involved was a roofing contractor.

October 11th	Mining		Holloway	Power line contact.  No other details given.

1006593				Township

October 16th	Construction	Toronto		Bobcat with hydraulic ram contacted a buried hydro line.

1006949

October 17th	Construction	Mississauga	Power line contact, no other information given.

1006885

October 23rd	Mining		Copper Cliff	Pole for trolley line caught fire when a wind blew sparks from

1007115						molten slag towards the pole.

October 24th	Industrial	Mississauga	Boom arm of garbage truck contacted an overhead line.

1007555

October 24th	Construction	Richmond	Backhoe dug up a buried line.  Locates had been done, did not

1010080						find the cable.

October 25th	Construction	Milton		Dump truck contacted a power line.

1009033

October 29th	Construction	Brantford	Tower crane contacted a 240 volt overhead line.

1007200

November 1st	Construction	Ottawa		Boom of a shovel contacted a 27.6 kV overhead line.

1008595

November 9th	Construction	Copper Cliff	Electrical contact made, lines knocked down.  No information

1007605						given as to type of equipment involved.

November 13th	Construction	Toronto		Electrical contact made, lines burnt off.  No information given

1007693						as to type of equipment involved.

November 14th	Construction	Sarnia		Crane struck the neutral of a 4800 volt overhead line.

1009402

November 15th	Construction	Niagara Falls	Hydro contact, no other information given.

1008148

November 16th	Construction	Newmarket	Dump truck struck energized hydro line.

1000121

November 20th	Construction	Thunder Bay	Excavator was digging for foundations, severed a 4160 volt

1001462				District		line.

November 20th	Construction	Pt. Colborne	Rock driller contacted a 2400 volt overhead line.

1008807

November 20th	Industrial	St. Catherines	Worker was doing tree trimming, branch came down on

1008916						line, knocked off the power.

November 22nd	Mining		Sudbury		Rebound muck from a blast hit an electrical cable.

1007992						Outage happened, cable was damaged.

November 22nd	Construction	Cambridge	Power lines contacted, no other details of incident given.

1008236

November 27th	Industrial	Hamilton	Fork-lift driver hit a ground wire for a hydro pole.  Two plants

1009048						shut down while repairs were made.

December 4th	Construction	Whitby		Crane contacted 13.8 kV overhead line.  No spotter for crane.

1008311

December 10th	Construction	Brampton	Contractor was doing directional drilling, dug into a 8 kV

1008504						cable.  Sensors on equipment automatically shut it off.

December 11th	Construction	Toronto		Contractor was laying underground cable, contacted hydro

1008541						line.

December 17th	Construction	Ingersoll		Worker cutting through a wall to install a dryer vent, cut

1008687						through the hydro services.

December 18th	Construction	Toronto		Hydro cable was cut by a drill.

1009943

December 19th	Construction	Sudbury		An excavator contacted a 7200 volt overhead line.

1008793

Reportable Incidents - Electrical Equipment:

November 28th	Construction	Nanticoke	Worker was working on a locked out breaker.  Something fell

1008533						into the live bus, arc occurred.  No injuries reported.

# DATA SUMMARY - Fourth Quarter

Fatals:		Criticals:	Non-criticals:		Powerline	Electrical

Contacts:	Equipment:

2001		     4*		      9		        28			      34		        1

2000		     2		      8		        15			      30		        1

1999		     2		      7		        21			      30		        1

1998		     1		      8		        15			      29		        2

* one of the fatal accidents in 2001 resulted in two electrocution deaths.

Information taken from MIS database,  February 18, 2002

Produced by:	Michael Reiser

Engineer

PSS – Kitchener District

Phone:	(519) 883-5682

FAX:	(519) 883-5694

E-Mail:	mike.reiser@mol.gov.on.ca